## Slide 1
Electric Field Analysis of 9-Tonne Railway Insulator by Finite Element Method
By
K.Mounika(18021D0803)
M.Tech (High Voltage Engineering)
Under the Esteemed Guidance of
Dr. M.Nageswara Rao M.Tech., Ph.D
University College of Engineering(A) Kakinada
JNTU Kakinada

## Slide 2
Module 1 | Literature Review | Study of RDSO specification for railway insulators. Study of various IEC and IS standards. Numerical Methods. FEMM-2D Software Study of various pollutions exits in the environment and their severity. | Completed
Module 2 | Design of 9-tonne Polymer Insulator | Geometrical Configurations of Polymer insulator Design of insulator model Polluted zone (ie.,Creapage Distance: 1050mm) Very Heavy Polluted zone (ie.,Creapage Distance: 1600mm) Electrical Field Intensity Results at critical regions of the insulator. Results Comparison. | Completed
Module 3 | Evaluation of Insulator Performance under various Contaminations | Polluted zone insulator Cement Contamination Urea Contamination Salt Contamination Very heavy polluted zone insulator Cement Contamination Urea Contamination Salt Contamination Electrical Field Intensity Results at critical regions of the insulator. Results Comparison. | Completed
Module 4 | Evaluation of Insulator Performance with water molecules | Polluted zone insulator With equal water molecules With unequal water molecules Very heavy polluted zone insulator With equal water molecules With unequal water molecules Electrical Field Intensity Results at critical regions of the insulator. Results Comparison. | Completed

## Slide 3
Module 5 | Evaluation of Insulator Performance with water molecules and under various Contaminations | Polluted zone insulator With Salt contamination and equal water molecules With Salt contamination and unequal water molecules With Cement contamination and equal water molecules With Cement contamination and unequal water molecules With Urea contamination and equal water molecules With Urea contamination and unequal water molecules Very heavy polluted zone insulator With Salt contamination and equal water molecules With Salt contamination and unequal water molecules With Cement contamination and equal water molecules With Cement contamination and unequal water molecules With Urea contamination and equal water molecules With Urea contamination and unequal water molecules Electrical Field Intensity Results at critical regions of the insulator. Results Comparison. | Completed
Module 6 | Results Comparison and Documentation | Electrical Field Intensity Results Comparison Documentation. | Completed

## Slide 4
25kV 9-Tonne polymer railway insulator designed using FEMM 2D software package.
Electric field analysis(EFA)is to be carried in the following cases:
  Polluted zone (ie.,1050mm Creepage Distance)
  Very Heavy Polluted zone (1600mm Creepage Distance)
Electrical Field Intensity Results at critical regions of the insulator Compared.
Various pollution contaminations and water molecules are on the polymer insulator tested and compared by using FEMM 2D software package.
Objective

## Slide 5: Introduction:
Insulators for railway traction applications are a category apart from the regular insulators as they demand extremely stringent performance and safety requirements.
Indian railways network typically uses three major types of insulators using composite and porcelain material they are: Stay Arm, Bracket tube and 9 Tonne insulators.
In this work, 9 tonne railway polymer insulators are designed and electric field intensity is analysed with the help of FEMM-2D software package. This software analyses the field intensity with the help of Finite Element Method.
In this work, two pollution zone insulators are considered (ie.1050mm and 1600mm creepage distance) Polluted and very heavy polluted zone insulators will be designed with FEMM-2D software package and various pollution performances are also analysed for an insulators.

## Slide 6
Used at each end of a 1.5 km section of weight-tensioned catenary. As the name implies, this has to withstand the combined tension forces in the catenary and contact wires .
It is also used in a vertical position to support 25kv feeder wire
9-Tonne Insulator:

## Slide 7: Pollution exists in environment and their severity:
Exposed insulators are subject to surface dirt deposits to some degree in all operating areas. Fog, mist, or light rain can usually create conditions that produce a conducting film on the dirty insulator surface, without washing the impurities from the surface.
These contaminants are distinguished primarily by the source of the impurities. Local agricultural, industrial, and geographic conditions determine what are present in the atmosphere.
The various types of contaminants identified include salt, cement/lime, dusts, bird excrement, chemicals, smog (automobile emissions), cooling tower effluents, smoke, and organic and ice/snow. Ordinarily, wind and rain provide sufficient washing action to remove most of the common deposits.
More than one of these contaminants may be deposited on a group of insulators at a particular location. The mix and rates of deposit of these contaminants determine the characteristics of the mixture . Main parts of disc, glass and ceramic insulators .
  Insulator pollution by bird excreta
  dust settlement on the surface and inside of insulators

## Slide 8
Polluted zone(CD-1050mm) i.e. 20mm/kV
These insulators shall be used in the areas, where equivalent salt deposit (ESDD) is <=0.3mg/sq.cm.
Very Heavy Polluted zone(CD-1600mm) i.e. 31mm/kV
These insulators shall be used in heavily/ very heavily polluted zones , where equivalent salt deposit density (ESDD) is more than 0.3 mg/sq.cm.

## Slide 9
  2D triangular elements are assigned to the model.
  These elements distributed throughout the model and its boundary.
  By running the model, contours will form throughout and surrounding area of the model.
2D Triangular elements:

## Slide 10: Module II
Design of 9-tonne Polymer Insulator

## Slide 11: Geometrical configuration: a)Polluted zone insulator(CD-1050mm:20mm/kV):
Table 1:specifications of insulator
 | polluted zone (mm)
FRP Length | 450
Total Length | 600
FRP Diameter | 32
Core Diameter | 38
Pitch | 60
Big Shed diameter | 120
Small Shed diameter | 90
Fig 1:9-Tonne polymer insulator

## Slide 12: b)Very Heavy Polluted zone insulator(CD-1600mm:31mm/kV):
.
Table 2:specifications of insulator
.
Fig 2:very heavy polluted insulator
 | Very Heavy polluted zone (mm)
FRP Length | 450
Total Length | 600
FRP Diameter | 32
Core Diameter | 38
Pitch | 60
Big Shed diameter | 180
Small Shed diameter | 140

## Slide 13: Material Properties :
Table 3:materials properties insulator
Assigning Boundary Conditions:
Minimum wet power frequency withstand voltage 100kV to the energized high voltage end fitting and 0V to the grounded end fitting of the insulator.
Material | Relative permittivity
Air | 1
Steel | 1
FRP | 5
Si | 3

## Slide 14: 2D Triangular elements of Polluted zone insulator:
Fig 3: 2D triangular elements
Fig 4: at HV end

## Slide 15: 2D Triangular elements of very heavy polluted zone insulator:
Fig 5: 2D triangular elements
Fig 6:at HV end

## Slide 16: Polluted zone EFI results:
Fig 7:contours at HV end
Table 4:EFI results
S.No | particulars | Electric Field Intensity(EFI) (kV/mm)
1 | CD | 0.217
2 | Triple Point | 0.284
3 | First Shed | 0.116
4 | Inside FRP | 0.348
5 | Inside Si | 0.144

## Slide 17: Very Heavy Polluted zone EFI results:
Fig 8:contours at HV end
Table 5:EFI results
S.No | particulars | Electric Field Intensity(EFI) (kV/mm)
1 | CD | 0.207
2 | Triple Point | 0.231
3 | First Shed | 0.130
4 | Inside FRP | 0.348
5 | Inside Si | 0.145

## Slide 18: EFI Results Comparison:
Table 6:EFI results of polluted and very heavy polluted zone insulator.
S.No | particulars | Polluted zone kV/mm | Very Heavy Polluted zone kV/mm
1 | CD | 0.217 | 0.207
2 | Triple Point | 0.284 | 0.231
3 | First Shed | 0.116 | 0.130
4 | Inside FRP | 0.348 | 0.348
5 | Inside si | 0.144 | 0.145
Chart: 
| CD | Triple point | First Shed | inside frp | inside si
1050mm | 0.217 | 0.284 | 0.116 | 0.348 | 0.144
1600mm | 0.207 | 0.231 | 0.13 | 0.348 | 0.145

## Slide 19: Module III
Evaluation of Insulator Performance under various Contaminations

## Slide 20: Material Properties :
Table 7:materials properties
Material | Relative permittivity
Cement | 2.7
Urea | 3.5
Salt | 6.1
Insulator Performance under various Contaminations:
a)Polluted zone insulator
  1. Cement Contamination
  2. Urea Contamination
  3. Salt Contamination
b)Very heavy polluted zone insulator
  1.Cement Contamination
  2.Urea Contamination
  3.Salt Contamination
  For EFI analysis, considering the contamination on the insulator to be even and uneven with 1mm and 0.5 thickness.

## Slide 21
Fig 9:contours for even 0.5mm thickness contamination
Fig 10:contours for even 1mm thickness contamination
Fig 8:contours for uneven 1mm thickness contamination
a)Polluted Zone :
1.Cement contamination
Fig 11:contours uneven 0.5mm thickness contamination

## Slide 22
Fig 13:contours for even 0.5mm thickness contamination
Fig 15:contours for even 1mm thickness contamination
Fig 14:contours for uneven 0.5mm thickness contamination
Fig 16:contors for uneven 1mm thickness contamination
a) Very Heavy Polluted Zone :
1.Cement contamination

## Slide 23
S.No | particulars | Polluted zone |  |  |  | Very heavy polluted zone |  |  | 
 |  | 0.5mm Even ctmn | 1mm Even ctmn | 0.5mm uneven ctmn | 1mm uneven ctmn | 0.5mm Even ctmn | 1mm Even ctmn | 0.5mm uneven ctmn | 1mm uneven ctmn
1 | CD | 0.241 | 0.244 | 0.229 | 0.232 | 0.224 | 0.226 | 0.218 | 0.220
2 | Triple Point | 0.184 | 0.172 | 0.276 | 0.270 | 0.185 | 0.146 | 0.239 | 0.238
3 | First shed | 0.136 | 0.136 | 0.142 | 0.142 | 0.144 | 0.144 | 0.145 | 0.145
EFI Results:
Table 8:EFI results of insulator with cement contamination
 | CD | TRIPLE POINT | FIRST SHED
1050mm | 0.217 | 0.284 | 0.116
1600mm | 0.207 | 0.231 | 0.130

## Slide 24
a 2)Urea contamination
Fig 17:contours for even 0.5mm thickness contamination
Fig 19:contours for uneven 0.5mm thickness contamination
Fig 20:contours for uneven 1mm thickness contamination
Fig 18:contours for even 1mm thickness contamination

## Slide 25
b 2) Urea contamination
Fig 21:contours for even 0.5mm thickness contamination
Fig 23:contours for uneven 0.5mm thickness contamination
Fig 22:contours for even 1mm thickness contamination
Fig 24:contours for uneven 1mm thickness contamination

## Slide 26: EFI Results:
S.No | particulars | Polluted zone |  |  |  | Very heavy polluted zone |  |  | 
 |  | 0.5mm Even ctmn | 1mm Even ctmn | 0.5mm uneven ctmn | 1mm uneven ctmn | 0.5mm Even ctmn | 1mm Even ctmn | 0.5mm uneven ctmn | 1mm uneven ctmn
1 | CD | 0.266 | 0.276 | 0.253 | 0.259 | 0.235 | 0.252 | 0.224 | 0.227
2 | Triple Point | 0.164 | 0.150 | 0.278 | 0.270 | 0.172 | 0.159 | 0.239 | 0.238
3 | First shed | 0.132 | 0.139 | 0.142 | 0.142 | 0.140 | 0.144 | 0.142 | 0.144
Table 9:EFI results of insulator with urea contamination
 | CD | TRIPLE POINT | FIRST SHED
1050mm | 0.217 | 0.284 | 0.116
1600mm | 0.207 | 0.231 | 0.130

## Slide 27
a3) Salt contamination
Fig 26:simulation results for even 1mm thickness contamination
Fig 25:contours for even 0.5mm thickness contamination
Fig 27:simulation results for uneven 0.5mm thickness contamination
Fig 28:simulation results for uneven 1mm thickness contamination

## Slide 28
b 3)Salt contamination
Fig29:contours for even 0.5mm thickness contamination
Fig30:contours for even 1mm thickness contamination
Fig32:contours for uneven 1mm thickness contamination
Fig31:contours for uneven 0.5mm thickness contamination

## Slide 29: EFI Results:
s.No | particulars | Polluted zone |  |  |  | Very heavy polluted zone |  |  | 
 |  | 0.5mm Even ctmn | 1mm Even ctmn | 0.5mm uneven ctmn | 1mm uneven ctmn | 0.5mm Even ctmn | 1mm Even ctmn | 0.5mm uneven ctmn | 1mm uneven ctmn
1 | CD | 0.328 | 0.360 | 0.258 | 0.261 | 0.288 | 0.316 | 0.230 | 0.234
2 | Triple Point | 0.129 | 0.112 | 0.273 | 0.274 | 0.146 | 0.131 | 0.233 | 0.233
3 | First shed | 0.130 | 0.141 | 0.148 | 0.146 | 0.142 | 0.149 | 0.148 | 0.149
Table 10:EFI results of an insulator with salt contamination
 | CD | TRIPLE POINT | FIRST SHED
1050mm | 0.217 | 0.284 | 0.116
1600mm | 0.207 | 0.231 | 0.130

## Slide 30
S.No | SALT | UREA | CEMENT
1050:0.5 mm | 0.328 | 0.266 | 0.241
1050: 1mm | 0.360 | 0.276 | 0.244
1600: 0.5 mm | 0.288 | 0.235 | 0.224
1600: 1mm | 0.316 | 0.252 | 0.226
S.No | SALT | UREA | CEMENT
1050:0.5 mm | 0.258 | 0.253 | 0.229
1050: 1mm | 0.261 | 0.259 | 0.232
1600: 0.5 mm | 0.230 | 0.224 | 0.218
1600: 1mm | 0.234 | 0.227 | 0.220
Results Comparison:
c)EFI (kV/mm): With uneven contamination
Table 11, 12 & 13:EFI results of an insulator without and with different contaminations
From the above table, the EFI of insulator with even contamination is about 51%,22% and 11% more compared to the insulator
without contamination. And with insulator which contains salt contamination have more EFI and the insulator with even contamination have more EFI compared to has uneven contamination.
Particular | 1050mm | 1600mm
CD | 0.217 | 0.207
a)EFI (kV/mm): Without Contamination
b)EFI (kV/mm): With even contamination

## Slide 31
Chart: 
| 1050:0.5mm | 1050:1mm | 1600:0.5mm | 1600:1mm
salt | 0.328 | 0.36 | 0.288 | 0.316
urea | 0.266 | 0.276 | 0.235 | 0.252
cement | 0.241 | 0.244 | 0.224 | 0.226
Chart: 
| 1050:0.5 mm | 1050: 1mm | 1600: 0.5 mm | 1600: 1mm
salt | 0.258 | 0.261 | 0.23 | 0.234
ura | 0.253 | 0.259 | 0.224 | 0.227
cement | 0.229 | 0.232 | 0.218 | 0.22
a)EFI (kV/mm): Even contamination
b)EFI (kV/mm): Uneven contamination

## Slide 32: Module IV
Evaluation of Insulator Performance with water molecules

## Slide 33: Material Property:
Water relative permittivity
Insulator Performance with water molecules
  a)Polluted zone insulator
    1.With equal water molecules
    2.With unequal water molecules
  b)Very heavy polluted zone insulator
    1.With equal water molecules
    2.With unequal water molecules
81

## Slide 34: a)Polluted zone
Fig34:contours results for unequal water molecules
Fig33:contours results for equal water molecules
1.With equal water molecules:
2.With unequal water molecules:

## Slide 35: b)Very Heavy Polluted zone
Fig36:contours results for unequal water molecules
Fig35:contours results for equal water molecules
1.With equal water molecules:
2.With unequal water molecules:

## Slide 36: EFI Results Comparison:
S.No | particulars | Polluted zone |  | Very heavy polluted zone | 
 |  | Equal water molecules | Unequal water molecules | Equal water molecules | Unequal water molecules
1 | CD | 0.225 | 0.232 | 0.223 | 0.228
2 | Triple Point | 0.268 | 0.270 | 0.248 | 0.236
3 | First shed | 0.144 | 0.146 | 0.144 | 0.146
Table 14 : EFI results of an insulator with water molecules
Chart: 
| CD | Triple Point | First Shed
1050: equal water molecules | 0.225 | 0.268 | 0.144
1050: unequal water molecules | 0.232 | 0.27 | 0.146
1600: equal water molecules | 0.223 | 0.248 | 0.144
1600: unequal water molecules | 0.228 | 0.236 | 0.146

## Slide 37: Module V
Evaluation of Insulator Performance with water molecules and under various Contaminations

## Slide 38: Insulator Performance with water molecules and under various Contaminations:
Case 1)Polluted zone insulator
  a)With Salt contamination and equal water molecules
  b)With Salt contamination and unequal water molecules
  c)With Cement contamination and equal water molecules
  d)With Cement contamination and unequal water molecules
  e)With Urea contamination and equal water molecules
  f)With Urea contamination and unequal water molecules
b)Very heavy polluted zone insulator
  a)With Salt contamination and equal water molecules
  b)With Salt contamination and unequal water molecules
  c)With Cement contamination and equal water molecules
  d)With Cement contamination and unequal water molecules
  e)With Urea contamination and equal water molecules
  f)With Urea contamination and unequal water molecules

## Slide 39
Case1:Polluted zone
  a)With Salt contamination and equal water molecules:
Fig 37:contours results for even 0.5mm ctmn with equal water molecules
Fig 38:contours results for uneven 0.5mm ctmn with equal water molecules
Fig 40:contours results for uneven 1mm ctmn with equal water molecules
Fig 39:contours results for even 1mm ctmn with equal water molecules

## Slide 40
b)With Salt contamination and unequal water molecules
Fig41:contours results for even 0.5mm ctmn with unequal water molecules
Fig 42:contours results for uneven 0.5mm ctmn with unequal water molecules
Fig 44:contours results for uneven 1mm ctmn with unequal water molecules
Fig 43:contours results for even 1mm ctmn with unequal water molecules

## Slide 41
c)With Cement contamination and equal water molecules:
Fig 46:contours results for uneven 0.5mm ctmn with equal water molecules
Fig 45:contours results for even 0.5mm ctmn with equal water molecules
Fig 47:contours results for even 1mm ctmn with equal water molecules
Fig 48:contours results for uneven 1mm ctmn with equal water molecules

## Slide 42
d)With Cement contamination and unequal water molecules:
Fig 49:contours results for even 0.5mm ctmn with unequal water molecules
Fig 51:contours results for even 1mm ctmn with unequal water molecules
Fig 52:contours results for uneven 1mm ctmn with unequal water molecules
Fig 50:contours results for uneven 0.5mm ctmn with unequal water molecules

## Slide 43
e)With Urea contamination and equal water molecules:
Fig 53:contours results for even 0.5mm ctmn with equal water molecules
Fig 55:contours results for even 1mm ctmn with equal water molecules
Fig 54:contours results for uneven 0.5mm ctmn with equal water molecules
Fig 56:contours results for uneven 1mm ctmn with equal water molecules

## Slide 44
f)With Urea contamination and unequal water molecules:
Fig 57:contours results for even 0.5mm ctmn with unequal water molecules
Fig 59:contours results for even 1mm ctmn with unequal water molecules
Fig 60:contours results for uneven 1mm ctmn with unequal water molecules
Fig 58:contours results for uneven 0.5mm ctmn with unequal water molecules

## Slide 45
s.No | particulars | Salt contamination and Equal water molecules |  |  |  | Salt contamination and Unequal water molecules |  |  | 
 |  | 0.5mm even | 1mm even | 0.5 mm uneven | 1mm uneven | 0.5mm even | 1mm even | 0.5 mm uneven | 1mm uneven
1 | CD | 0.334 | 0.363 | 0.308 | 0.314 | 0.312 | 0.336 | 0.302 | 0.312
2 | Triple Point | 0.129 | 0.115 | 0.273 | 0.273 | 0.127 | 0.116 | 0.260 | 0.274
3 | First shed | 0.166 | 0.175 | 0.168 | 0.167 | 0.166 | 0.174 | 0.166 | 0.167
s.No | particulars | Cement contamination and Equal water molecules |  |  |  | Cement contamination and Unequal water molecules |  |  | 
 |  | 0.5mm even | 1mm even | 0.5 mm uneven | 1mm uneven | 0.5mm even | 1mm even | 0.5 mm uneven | 1mm uneven
1 | CD | 0.245 | 0.245 | 0.253 | 0.259 | 0.235 | 0.240 | 0.252 | 0.261
2 | Triple Point | 0.185 | 0.171 | 0.268 | 0.270 | 0.180 | 0.171 | 0.258 | 0.270
3 | First shed | 0.158 | 0.159 | 0.160 | 0.159 | 0.156 | 0.156 | 0.154 | 0.159
s.No | particulars | Urea contamination and Equal water molecules |  |  |  | Urea contamination and Unequal water molecules |  |  | 
 |  | 0.5mm even | 1mm even | 0.5 mm uneven | 1mm uneven | 0.5mm even | 1mm even | 0.5 mm uneven | 1mm uneven
1 | CD | 0.268 | 0.278 | 0.260 | 0.264 | 0.256 | 0.262 | 0.254 | 0.259
2 | Triple Point | 0.165 | 0.150 | 0.269 | 0.268 | 0.164 | 0.150 | 0.258 | 0.270
3 | First shed | 0.157 | 0.180 | 0.160 | 0.159 | 0.156 | 0.160 | 0.160 | 0.159
Table 15, 16 & 17: EFI results of an insulator with diff contaminations (salt, cement & urea) and water molecules (equal & unequal)
EFI Results:

## Slide 46
Case2: Very Heavy Polluted zone
  a)With Salt contamination and equal water molecules:
Fig 61:contours results for even 0.5mm ctmn with equal water molecules
Fig 62:contours results for uneven 0.5mm ctmn with equal water molecules
Fig 63:contours results for even 1mm ctmn with equal water molecules
Fig 64:contours results for uneven 1mm ctmn with equal water molecules

## Slide 47
b)With Salt contamination and unequal water molecules:
Fig 65:contours results for even 0.5mm ctmn with unequal water molecules
Fig 66:contours results for uneven 0.5mm ctmn with unequal water molecules
Fig 68:contours results for uneven 1mm ctmn with unequal water molecules
Fig 67:contours results for even 1mm ctmn with unequal water molecules

## Slide 48
Fig 69:scontours results for even 0.5mm ctmn with equal water molecules
Fig 71:contours results for even 0.5mm ctmn with equal water molecules
Fig 70: contours results for even 0.5mm ctmn with equal water molecules
Fig 72:contours results for even 0.5mm ctmn with equal water molecules
c)With Cement contamination and equal water molecules:

## Slide 49
d)With Cement contamination and unequal water molecules:
Fig 73:contours results for even 0.5mm ctmn with unequal water molecules
Fig 74:contours results for uneven 0.5mm ctmn with unequal water molecules
Fig 76:contours results for uneven 1mm ctmn with unequal water molecules
Fig 75:contours results for even 1mm ctmn with unequal water molecules

## Slide 50
e)With Urea contamination and equal water molecules:
Fig 77:contours results for even 0.5mm ctmn with equal water molecules
Fig 79:contours results for even 0.5mm ctmn with equal water molecules
Fig 80:contours results for even 0.5mm ctmn with equal water molecules
Fig 78:contours results for even 0.5mm ctmn with equal water molecules

## Slide 51
f)With Urea contamination and unequal water molecules:
Fig 81:contours results for even 0.5mm ctmn with unequal water molecules
Fig 83:contours results for even 1mm ctmn with unequal water molecules
Fig 84:contours results for uneven 1mm ctmn with unequal water molecules
Fig 82:contours results for uneven 0.5mm ctmn with unequal water molecules

## Slide 52
s.No | particulars | Salt contamination and Equal water molecules |  |  |  | Salt contamination and Unequal water molecules |  |  | 
 |  | 0.5mm even | 1mm even | 0.5 mm uneven | 1mm uneven | 0.5mm even | 1mm even | 0.5 mm uneven | 1mm uneven
1 | CD | 0.300 | 0.338 | 0.296 | 0.307 | 0.292 | 0.334 | 0.283 | 0.298
2 | Triple Point | 0.148 | 0133 | 0.246 | 0.243 | 0.149 | 0.132 | 0.250 | 0.244
3 | First shed | 0.140 | 0.142 | 0.154 | 0.156 | 0.145 | 0.142 | 0.154 | 0.155
S.No | particulars | Cement contamination and Equal water molecules |  |  |  | Cement contamination and Unequal water molecules |  |  | 
 |  | 0.5mm even | 1mm even | 0.5 mm uneven | 1mm uneven | 0.5mm even | 1mm even | 0.5 mm uneven | 1mm uneven
1 | CD | 0.226 | 0.231 | 0.229 | 0.232 | 0.225 | 0.228 | 0.231 | 0.234
2 | Triple Point | 0.186 | 0.177 | 0.224 | 0.241 | 0.186 | 0.179 | 0.253 | 0.243
3 | First shed | 0.140 | 0.141 | 0.147 | 0.148 | 0.145 | 0.140 | 0.190 | 0.150
S.No | particulars | Urea contamination and Equal water molecules |  |  |  | Urea contamination and Unequal water molecules |  |  | 
 |  | 0.5mm even | 1mm even | 0.5 mm uneven | 1mm uneven | 0.5mm even | 1mm even | 0.5 mm uneven | 1mm uneven
1 | CD | 0.246 | 0.256 | 0.244 | 0.249 | 0.248 | 0.258 | 0.247 | 0.253
2 | Triple Point | 0.174 | 0.161 | 0.246 | 0.242 | 0.173 | 0.162 | 0.243 | 0.243
3 | First shed | 0.136 | 0.140 | 0.147 | 0.148 | 0.142 | 0.138 | 0.168 | 0.148
EFI Results:
Table 18, 19 & 20: EFI results of an insulator with diff contaminations (salt, cement & urea) and water molecules (equal & unequal)

## Slide 53
S.No | Contamination | Equal water molecules |  |  |  | Unequal water molecules |  |  | 
 |  | 0.5mm even | 1mm even | 0.5 mm uneven | 1mm uneven | 0.5mm even | 1mm even | 0.5 mm uneven | 1mm uneven
1 | Salt | 0.334 | 0.363 | 0.308 | 0.314 | 0.312 | 0.336 | 0.302 | 0.312
2 | Urea | 0.268 | 0.278 | 0.260 | 0.264 | 0.256 | 0.262 | 0.254 | 0.261
3 | Cement | 0.242 | 0.245 | 0.253 | 0.259 | 0.235 | 0.240 | 0.252 | 0.258
S.No | Contamination | Equal water molecules |  |  |  | Unequal water molecules |  |  | 
 |  | 0.5mm even | 1mm even | 0.5 mm uneven | 1mm uneven | 0.5mm even | 1mm even | 0.5 mm uneven | 1mm uneven
1 | Salt | 0.300 | 0.338 | 0.296 | 0.307 | 0.292 | 0.324 | 0.283 | 0.298
2 | Urea | 0.246 | 0.256 | 0.244 | 0.249 | 0.248 | 0.258 | 0.247 | 0.253
3 | Cement | 0.226 | 0.231 | 0.229 | 0.232 | 0.225 | 0.228 | 0.231 | 0.234
a)Polluted zone:
b)Very Heavy Polluted zone:
EFI Results Comparison:
Table 21 & 22: EFI results of an insulator with diff contaminations (salt, cement & urea) and water molecules (equal & unequal)
The severity of stress is increase with the combination of contamination and water molecules.

## Slide 54
Chart: 
| Salt | Urea | Cement
0.5 even | 0.334 | 0.268 | 0.242
1even | 0.363 | 0.278 | 0.245
0.5uneven | 0.308 | 0.26 | 0.253
1uneven | 0.314 | 0.264 | 0.259
Chart: 
| Salt | Urea | Cement
0.5even | 0.312 | 0.256 | 0.235
1even | 0.336 | 0.262 | 0.24
0.5uneven | 0.302 | 0.254 | 0.252
1uneven | 0.312 | 0.261 | 0.258
Chart: 
| Salt | Urea | Cement
0.5even | 0.3 | 0.246 | 0.226
1even | 0.338 | 0.256 | 0.231
0.5uneven | 0.296 | 0.244 | 0.229
1uneven | 0.307 | 0.249 | 0.232
Chart: 
| Salt | Urea | Cement
0.5even | 0.292 | 0.248 | 0.225
1even | 0.324 | 0.258 | 0.228
0.5uneven | 0.283 | 0.247 | 0.231
1uneven | 0.298 | 0.253 | 0.234
b)Polluted zone insulator with unequal water molecules
a)Polluted zone insulator with equal water molecules
c)Very heavy Polluted zone insulator with equal water molecules
d)Very heavy Polluted zone insulator with equal water molecules

## Slide 55: Conclusion:
Based on the simulation results it was concluded that electric field is greatly influenced by pollution layer conductivity and thickness.
As the pollution layer conductivity and thickness increases, EFI increases. The highest EFI observed in the case of 1mm thickness layer.
Salt is the most severe pollution contamination on polymer insulator.
When comes to water molecules on insulator, the stress level depend on the number of droplets, droplet width and diameter of the water droplet.
The severity of electric field stresses greatly increase, if the pollution contamination on insulator is combined with water molecules.

## Slide 56: References
M. Chen, T. Wen, W. Jiang and J. Luo, "Modelling and Simulation of New Traction Power Supply System in Electrified Railway," 2015 IEEE 18th International Conference on Intelligent Transportation Systems, Las Palmas, 2015, pp. 1345-1350.
T. Ohashi, Y. Asai, K. Kusagawa, K. Yamamoto and S. Sumi, "Overvoltage Response at Railway Insulators Based on Viaduct Configuration," 2019 11th Asia-Pacific International Conference on Lightning (APL), Hong Kong, 2019, pp. 1-5
Han Se-Won, Cho Han-Goo, Choi In-Hyuk and Lee Dong-Il. Failure characteristics of suspension-type porcelain insulators on a 154 kV transmission line. Electrical Insulation 2006. Proceedings of IEEE International Symposium June 2006, pp118-A.
Verdicchio, P. Ladoux, H. Caron and C. Courtois, "New Medium-Voltage DC Railway Electrification System," in IEEE Transactions on Transportation Electrification, vol. 4, no. 2, pp. 591-604, June 2018.
S. Pastromas, A. Papamikou, G. Peppas and E. Pyrgioti, "Investigation of grounding resistance effect on the MV grid of Hellenic electromotive railway during lightning strikes," 2016 33rd International Conference on Lightning Protection (ICLP), Estoril, 2016, pp. 1-7.
[15] F. Greuter, Y. Dirix, P. Kluge-Weiss, W. Schmidt, and R. Kessler, "Polymer compound with nonlinear current-voltage characteristic and process for producing a polymer compound", United States Patent 7320762, 2008. [16] R. Strumpler and P. Kluge-Weiss, "Smart varistor composites", 8th International Conference on Modern Materials and Technologies (CIMTEC)-World Ceramic Congress & Forum on New Materials, pp. 1522, Montecatini Terme (Italy), 1995.

## Slide 57
N. Yoshimura and S. Kumagai "Electrical and environmental aging of silicone rubber used in outdoor instalation”
IEEE Trans. Dielectr. Electr. Insul. vol. 6 pp. 632-650 1999.
J. S. Forest "The performance of high voltage insulators in polluted atmospheres" Proc. of IEEE Winter
Meeting 1969.
Nekahi S. Mcmeekin and M. Farzaneh "Effect of pollution severity on electric field distribution along a polymeric
insulator" 2015 IEEE 11th international conference on the properties and applications of dielectric
materials (ICPADM) 19–22 July 2015.
R.S. Gorur G.G. Karady A. Jagota M. Shah and A.M. Yates "Aging in silicone rubber used for outdoor insulation"
IEEE Transactions on Power Delivery vol. 7 pp. 525-538 April 1992.
H. Gao Z. Jia Y. Mao Z. Guan and L. Wang "Effect of hydrophobicity on electric field distribution and discharges along various wetted hydrophobic surfaces" IEEE Transaction on Dielectrics and Electrical Insulation vol. 15 pp.
435-443 April 2008.
R. Abd-Rahman A. Haddad N. Harid and H. Griffiths "Stress control on polymeric outdoor insulators
using zinc oxide microvaristor composites" IEEE Transaction on Dielectrics and Electrical Insulation
vol. 19 pp. 705-713 April 2012.
Fujimura T. The evolution of porcelain insulator technology in Japan. Electrical Insulation Magazine, IEEE Vol 11,Issue 3, May/Jun 1995 pp26-36.